## Slide 1: RF technology in SOLEIL II
Lu ZHAO
On Behalf of the RF & LINAC Group
and P. Marchand (scientific advisor)

## Slide 2: SOLEIL II
Objectives :
Address present and future scientific and societal challenges through a reconstruction of the storage ring with an emittance < 100 pm.rad, 100 times brighter beams and adapted beamlines.
Keep the broad energy range from THz to hard X-rays and almost all the operation modes of the present SOLEIL machine.
SOLEIL II reference planning

## Slide 3: Main SR parameters & fundamental RF specifications
ǂ Including 312 keV for the ID’s
* 2.8 MV in standard operation,
3.2 MV in low a mode (anom / 25)
** Without ID’s contribution
Loulergue, A., et al. "TDR baseline lattice for SOLEIL II upgrade project. 14th IPAC, Venice, Italy

## Slide 4: RF Activities
RF Cavities
  4 Normal Conducting (NC) ESRF-EBS type cavities (352MHz)
  Harmonic RF system (SC vs NC)
RF Power Amplifier and Distribution (Waveguide layout)
  SSA Power Supply Upgrade
  New Power plant layout
  Upgrade of the SSA supervision system
Low-Level RF (LLRF)
  Devices
  Analog Frond-End (AFE)
  Test at SOLEIL with 450mA beam

## Slide 5: 352 MHz fundamental cavities (MC)
Collaboration with ESRF to benefit from their EBS-type 352 MHz HOM-damped cavities  Plans and specifications that they used for their call for tender have been received
4 NC ESRF-EBS-type cavities will be necessary to provide redundancy (possibility to run with 3 cavities out of 4 in nominal 500 mA operation mode)
For ESRF EBS fondamental power coupler Pmax ~ 160 kW
 Collab. with CERN for LHC type power coupler (Pmax >> 200 kW)
 | 4 (3) NC cavities ESRF-EBS
Length [m] | ~ 4.20
Redundancy | Yes
VRF [MV] | 1.7 (1.6)
Pb [kW] | 398
Vcav [kV] | 425 (533)
Pdis [kW] | 4 x 18 (3 x 29)
Pcav [kW] | 118 (162)
Pcav [kW] | 150 (185)
Coupling | ßc = 5
RF parameters based on V0356 lattice including 312 keV ID loss
Passive
SC HC
NC HC

## Slide 6: Longitudinal impedance
Coupled bunch instabilities threshold calculation :
Danger mode @ 1,7 GHz
Its impedance is about 28% smaller than the LCBI threshold for 4 cavities (from the above approximate formula). However, it is about 15% higher than the anticipated reduced LCBI threshold with HC ( to be confirmed by further simulations).
CST
Possible cure:
Longitudinal Bunch-by-Bunch Feedback

## Slide 7
Chart: 
V [MV]
V1h = 1.7 MV
V3h = 0.53 MV
V1h + V3h
Long bunch
Long bunch
Bunch lengthening : phase and amplitude of V3h
adjusted such that the overall voltage is flat at s
For V3h  V1h / 3  0.53 MV, t  4 to  100 ps FWHM
SOLEIL II 3rd harmonic case
Main purpose :
Lengthen the bunches up to ~ 100 ps FWHM and thus reduce their charge density to preserve the low emittance and insure suitable beam lifetime
Initial specifications aimed at allowing :
  Short bunch production (~10 ps FWHM)  ~1.7 MV needed @ 3FRF
  Hybrid mode with asymmetric beam filling pattern
   transient beam loading (TBL) issues
Such high RF voltage requirement together with available space constraints along the ring and attempts to reduce TBL justified the choice of SC cavity technology as the most suitable one.
Harmonic RF system
But after the CDR, it was decided to remove from the baseline specification the option of producing short bunches (~10 ps FWHM) and the non-uniform beam filling patterns with long bunches (~100 ps FWHM) so NC technology option for harmonic system had to be investigated and compared to the SC one.

## Slide 8
SUPER3HC cryomodule
SC HC vs. NC HC
A SC HC version, based on a Super-3HC type Cryomodule @ 1.41 (or 1.06 GHz), has been evaluated in collaboration with CEA and CERN. In parallel, a NC HC version, based on an ESRF-EBS 1.41 GHz 2-cell cavity (or an assembly of two single-cell cavities), has been evaluated in collaboration with ESRF and KEK.
New operation mode specification for SOLEIL II : priority to high average current modes (500 mA in 416 bunches, uniformly filled and 200 mA in 32 bunches, evenly spaced).
Comparison resume
The passive SC remains the best option in terms of bunch lengthening factor (BLF) and operational « ease » but its investment cost is higher by about a factor 4 (~ 2 M€) as compared to the passive NC (~ 0.5 M€), which should provide lower, nevertheless acceptable, BLF for the 2 operation modes (500 mA in 416 bunches, 200 mA in 32 bunches) and moreover the best operational reliability (no RF power source, no cryogenics). The MC power margin is enough to compensate for the NC HC wall dissipation of about 50 kW at 500 kV.
The active NC HC (investment cost ~ 1 M€) is still under study; with RF feedbacks (RFFB), it could achieve comparable BLF as the passive SC ; however its operational control is much more critical (feasibility to be demonstrated).
Considering the new operation mode specification, energy price increase and budget constraints, we now consider the following two-phase strategy as the most attractive for the HC :
  Phase 1 : begin with 1 passive NC HC 4H of the ESRF-EBS type
  Phase 2 : after experience feedback, if needed, add a power coupler + power source (SSA based on GaN) to convert the passive cavity into an active one
SC HC vs. NC HC

## Slide 9: ESRF-EBS 4th HC (1.41 GHz)
LCBI threshold for SOLEIL II case with 1 cavity is a factor of almost 8 lower than ESRF-EBS case with 3 cavities !!
 Mitigations : HOM dampers and/or longitudinal b.b.b. feedback
2-cell cavity
Rs = 2,4 cav
= 36 000
= / cav
= 1
GDFIDL
Preliminary simulations show sufficient HOM attenuations by using 2 or 3 HOM dampers per cell
ESRF simulations in the framework of WP3 collaboration among ESRF, KEK, and SOLEIL – Design and implementation of a harmonic RF system with TBL compensation
w/o HC
with HC
w/o HC
with HC

## Slide 10: 352 MHz Power Sources
Objective : Reuse the four SSPA’s in the SOLEIL II SR, after power supply and supervision system upgrade + other adaptations, as for instance connecting each tower directly on the waveguide  Gain in flexibility.
Power supply upgrade : Rectifier + DC/DC converters replacement by direct AC/DC converters
Redundancy, easy maintenance, reduced time to repair, solved obsolescence issues and cost reduction
Efficiency improvement
Total actual efficiency = 87% (96% rectifier and 90% DC/DC converters)
Increased to 96% with new AC/DC converters
AC/DC converter voltage remote control allows to match for maximum efficiency over whole power range (impossible presently: components set to reach max efficiency only at max power – 1dB compression)
Power supply upgrade plan
From begining, 1 x 50 kW will be installed every 2-3 months in the SR to benefit from four fully upgraded 200 kW SSPA’S by the mid-2028 for SOLEIL II

## Slide 11: Power Supply Upgrade
8 x 3 kW power converters
5 x 24 kW AC/DC racks (19" 3U)
3D view of a future upgraded SSPA RF tower with new AC/DC power converters
Support pipes with bigger diameter, adapted to the new power supply weight
New dissipater orientation to optimize and reduce power cable length
5 x SSPA control rack (19" 1U)
Beam current | 450 mA | 500 mA
Overall RF power | 506 kW | 562 kW
Electric power (4 SSPA’s in present SOLEIL machine) | 1148 kW | 1278 kW
Electric power (4 upgraded SSPA’s @ 50 V) | 1019 kW | 1081 kW
Electric power (4 upgraded SSPA’s @ 44 V) | 894 kW | 952 kW
Maximum consomption reduction (44 V) | 22.1% | 25.5%
Power savings of 1.75 GWh max per year
250 k€ savings per year
Compensate the investment cost in ~ 4 years

## Slide 12: Power Supply Upgrade
Mezzanine measurement PCB
PCB mechanical support
Current measurements were initially done in the DC/DC converter.
New architecture  RF module modifications : Electronic mezzanine card for supervision (1 x T° sensor on circulator load to evaluate reflected power + 1 current sensor)
Module modifications

## Slide 13: Upgrade of the SSA supervision system
Architecture modification : 5 “secondary” µcontrollers per tower, all linked to 1”main” µcontroller for the complete amplifier

## Slide 14: Power Source layout
CM2
CM1
A4
A3
A2
A1
Present SOLEIL RF layout
4 SSPA’s & 2 cryomodules
SOLEIL II RF layout
4 SSPA’s & 4 NC cavities
4 MC

## Slide 15: Digital LLRF, we played with some devices …
AMC580
Vadatech VT812
ZC706 Zynq evaluation board
FMC-4CH-125 (Techway)
FMC224 (Vadatech)
Native-R2 µTCA platform, MCH-PHYS80 (NAT Europe)
DAMC-FMC2ZUP (CAENels)
FMC LXD31K4-DC 4 channel 16-bit ADC/DAC (Logic-X )

## Slide 16
Analog Frond-End (AFE)
Analog Frond-End(AFE) : the IQ measurement is performed at an Intermediate Frequency (IF) of 10 MHz, which is obtained through an active mixer (Analog Devices, ADL5801).
Jitter level of IF output: depends on the LO and RF signal level.

## Slide 17
D-LLRF test on SOEIL with 450mA beam
The phase noise of the cavity pickup signal is measured directly by the R&S FSUP+B60 option analyzer. It corresponds to 0.06 ps, which is as well as the present analog system.
Digital LLRF GUI
Client – Server model
Server
Client
Accuracy :
3×10-4/2.4×10-2° rms
Loop gain of 18
Successfully stored 450 mA beam with actual SOLEIL cavity.
LLRF2023 Gyeongju,
Republic of Korea

## Slide 18: Summary
SOLEIL II :
  352 MHz RF accelerating structures  4 x ESRF-EBS type cavities, simulation shows reasonable stability margin w.r.t longitudinal and transverse impedance thresholds for CBI
  Harmonic RF system  Favored option : Start with a NC passive HC of the ESRF-EBS type (1.41 GHz) and, in a 2nd phase, if needed, upgrade it towards an active system (Project of collaboration with ESRF)
  352 MHz power sources  reuse 4 x SSPA’s presently running at SOLEIL + Power Supply upgrade with new high efficiency AC/DC power converters to save up to 25.5% of electrical consumption while providing more redundancy
  Digital LLRF  a generic digital system, based on µTCA, which can be adapted to these RF systems (fundamental, harmonic), is being developed and validated.

## Slide 19: Thanks to the SOLEIL II project team